Solutions to EEL-3303 HW#1

2.17)     2x % is the tolerance  on the closed loop  ,-110.5<G<-90.5

  - R 1=1.49KΩ Ra=5.84kΩ

2-22) a) For a=∞ Vi=0 , Rm=-Rf  , Rin=0

b) For a=finite VI=-V0/Rf ,   Rm=- RF/1+1/a ,  Ri=Rf/1+a

2.33)  a) R=0.53kΩ

b) -0.4mA    ≤     ii  ≤    0.4Ma

c) iI=1Ma  , iL=20Ma

2.37) I 1, I 2 ≤0.1m A, r1=10kΩ  , Rf=40kΩ , R2=120kΩ

2-72)  i=0.08 sinωt mA   , Va=3+4.04 sinωt, v  ,Vb=3-4.04 sinωt, v  ,, Vc= 1.5-2.02 sinωt,

v , V0= -8.08 sinωt, v

2-87)  F 3DB =F t =1MHZ,f=0.142 mhz,τ=1/2Л μs  , Tr=0.35 μs

2-91)  a) GBP=kft /1+k

b) GBP=Ft  ----(  the non inverting amplifier realizes a higher GBP and its

independent of k

2-95)  The output is triangular with the slew rate of 20v/ μs .Inorder to reach 3v it takes

150ns .so the minimum pulse width is 150 ns

2-97) f= 250khz ,V0=6.37v

2.100)V0=3mv

2.104)  a)Ib1=930nA

b)Vos=-2.2mv

c)Ios=-80Na

2.118) V0=10mv ,a total of 100 pulses are reqired for a change of 1v

2.120)R3=9.9KΩ ,V0=0.313V

3-3)a) v=3v , i=3mA

b) v=1v , i=1mA

3.6)

3.15) peak to peak sine wave voltage=29.6v

peak diode current=0.75A

peak reverse voltage=26.83v

conduction starts at θ=0.93 rads  ,

fraction of cycle the current flows=20%

Average diode current=136Ma  , peak diode current =1A  ,peak reverse voltage=27 v

3.20) I S =3.46 x 10 -15  ∆V=57.56mV

| V | i |
| --- | --- |
| 0.71 v | 7.46 mA |
| 0.8V | 273.21 mA |
| 0.69V | 3.35 mA |
| 0.6V | 91.65 µA |

3.23) I= 3.81mA  , Δv=-22.8Mv

3-25) V=92.2 mv  , for  v=50 v  ,I2=5.75mA

3-32)

3-34) a) Id =1.5mA

b) iterative analysis given VD=0.7V AT iD=1 mA

# 1   v=0.7v  , id=1.5Ma

# 2   v= 0.716 , id=1.4mA

#3    v=0.716 v ,  id= 1.42mA

# 4 v=0.716 v ,  id=1.42mA

  - for v0=0.5 vs  , I=50Μa

3.68) V0= 7.55V , RLmin=1.04kΩ

3.78)

peak value of the rectified voltage=15.57v,Fraction of cycle the current flows is

=47.4%V0avg= 9.44v , Ir,avg=9.44mA

3.82)   Vs=24.66 v ,voltage across secondary winding is =49.32v , if choosing a didoe allow a safety margain of 73v

3.89)

a) vr=0.93v , v0 avg=8.84v

b)  Δt=0.02325 ms

c)Ic avg = 4 .0A Id avg =4.09A

d) Ic max=4A  ID max=4.09A

3-93)

3.100)