CURRENT-VOLTAGE CHARACTERISTICS

We will present the current voltage characteristic for DC to low frequency operation of the Enhancement type MOSFET.

Circuit Symbol

| Figure 4.10 (a) Circuit symbol for the n-channel enhancement-type MOSFET. (b) Modified circuit symbol with an arrowhead on the source terminal to distinguish it from the drain and to indicate device polarity (i.e., n channel). (c) Simplified circuit symbol to be used when the source is connected to the body or when the effect of the body on device operation is unimportant. |  |
| --- | --- |

The iD-vDS Characteristics

| Triode Region (induced Channel) Overdrive Saturation Region (induced Channel) ; Process Transconductance |  |
| --- | --- |

Saturation Region

Finite Output Resistance in Saturation

Characteristics of the p-Channel MOSFET

| Triode Region (induced Channel) Overdrive Saturation Region (induced Channel) ; Process Transconductance |  |
| --- | --- |

MOSFET CIRCUITS AT DC

Example 4.2

| Design for: Given |  |
| --- | --- |

Example 4.3

| Design for: Given |  |
| --- | --- |

Excersise 4.12

| Q1 and Q2 are identical, Find the drain current in Q2. |  |
| --- | --- |

Example 4.4

| Design for: Given |  |
| --- | --- |