satbv@SatBv:~$ bladeRF-cli -d libusb:serial=595bc103b11356bbb1b580a173bac13d -i
bladeRF> load fpga Downloads/hostedx40.rbf
Loading fpga from Downloads/hostedx40.rbf...
Done.
bladeRF> poke lms 0x09 0xc0
  0x09: 0xc0
bladeRF> set rxvga1 10
bladeRF> set rxcga2 10
set: Invalid parameter (rxcga2)
bladeRF> set rxvga2 10
bladeRF> mimo clk slave
Successfully set device to slave MIMO mode
bladeRF> quit

satbv@SatBv:~$ bladeRF-cli -d libusb:serial=771dcac5b27d49ae07e64eb04d169362 -i
bladeRF> load fpga Downloads/hostedx40.rbf
Loading fpga from Downloads/hostedx40.rbf...
Done.
bladeRF> poke lms 0x09 0xc0
  0x09: 0xc0
bladeRF> set rxvga1 10
bladeRF> set rxvga2 10
bladeRF> mimo clk slave
Successfully set device to slave MIMO mode

bladeRF-cli -d libusb:serial=a2b9a9a5f90e3be21a09473fc159b907 -i
bladeRF> load fpga Downloads/hostedx40.rbf
Loading fpga from Downloads/hostedx40.rbf...
Done.
bladeRF> poke lms 0x09 0xc0
  0x09: 0xc0
bladeRF> set rxvga1 10
bladeRF> set rxvga2 10
bladeRF> mimo clk slave
Successfully set device to slave MIMO mode

a2b9a9a5f90e3be21a09473fc159b907

ca2039c093a1282896527becf759b5c5

bladeRF-cli -d libusb:serial=ca2039c093a1282896527becf759b5c5 -i
bladeRF> load fpga Downloads/hostedx40.rbf
Loading fpga from Downloads/hostedx40.rbf...
Done.
bladeRF> poke lms 0x09 0xc0
  0x09: 0xc0
bladeRF> set rxvga1 10
bladeRF> set rxvga2 10
bladeRF> set smb_mode input
Successfully set device to slave MIMO mode

  Backend: libusb
  Serial: bc77060b20a7ed6e4f6df98aed598a9e
  USB Bus: 1
  USB Address: 47

  Backend: libusb
  Serial: a2b9a9a5f90e3be21a09473fc159b907
  USB Bus: 1
  USB Address: 46

  Backend: libusb
  Serial: 65da50a6be76cf0918e5b56776749c39
  USB Bus: 1
  USB Address: 45

  Backend: libusb
  Serial: ca2039c093a1282896527becf759b5c5
  USB Bus: 1
  USB Address: 40

bladeRF-cli -d libusb:serial=bc77060b20a7ed6e4f6df98aed598a9e -i

bladeRF-cli -d libusb:serial=a2b9a9a5f90e3be21a09473fc159b907 -i

bladeRF-cli -d libusb:serial=65da50a6be76cf0918e5b56776749c39 -i

bladeRF-cli -d libusb:serial=ca2039c093a1282896527becf759b5c5 -i

set smb_mode input

MASTER.tst

set frequency rx 922M
set frequency tx 923M
set samplerate 6M
set bandwidth 3M
set txvga1 -15
set txvga2 0
set lnagain 6
set rxvga1 10
set rxvga2 0

# Configure TX & RX operations
tx config file=master_tx.csv format=csv repeat=25 timeout=60s
rx config file=master_rx.csv format=csv n=60000 timeout=60s

# Output reference clock
set smb_mode output

# Arm the triggers
trigger j71-4 tx master
trigger j71-4 rx slave

# Start streaming sampling
rx start
tx start

# Inform user how to fire trigger
echo " ---------------------------------------------------------------"
echo " Run the slave.txt script in another terminal."
echo " Then, run 'trigger j71-4 tx fire' to fire trigger."
echo " ---------------------------------------------------------------"
echo ""

SLAVE.txt

set frequency rx 922M
set frequency tx 922M
set samplerate 6M
set bandwidth 3M
set lnagain 6
set rxvga1 10
set rxvga2 0

# Configure RX & TX operations
rx config file=slave_rx.csv format=csv n=60000 timeout=60s

# Use reference clock input from master.
# This assumes the master is already outputting this reference.
set smb_mode input

# Arm the trigger
trigger j71-4 rx slave

# Start streaming sampling
rx start

# Inform user how to fire trigger
echo " ---------------------------------------------------------------"
echo " Ready. Fire the trigger on the master device."
echo " ---------------------------------------------------------------"

# Wait for the RX to complete and then finish up.
rx wait

Synchronized TRX
This example illustrates how to synchronize RX and TX sampling on multiple devices, using the bladeRF-cli and the trigger functionality introduced in FPGA v0.6.0.
This example assumes the use of an RF power splitter/combiner and two bladeRF devices, connected as follows:
1. The "master" bladeRF has both its TX and RX ports connected to the combiner.
2. The "slave" bladeRF has its RX port connected to the combiner.
3. Pin 4 on J71 on both devices is connected together. This connects the trigger signal on both devices. The "master" will output this signal, and the "slave" will receive it.
4. Pin 2 on J71 on both devices is connected. This provides a common ground.
5. The J62 SMB clock connector of both devices are connected together. The "master" bladeRF will output its 38.4 MHz reference clock, and the "slave" bladeRF will utilize this reference instead of its own on-board clock. This ensures that both devices are sampling using the same clock.
When a trigger is "armed," the FPGA will gate both transmit and receive samples; the flow of samples to/from the host is blocked. The assertion ("firing") of the trigger signal unblocks samples, causing all devices to begin transmitting or receiving within +/- 1 sample clock period.
In this example, the "master" will transmit a series of on-off pulses at a 1 MHz offset, and both the "master" and "slave" will receive these pulses. The transmission and reception are synchronized using the J71-4 trigger signal.
Creating Samples
Scripts are provided to create a samples.csv file containing a single pulse. This files consists of 1,000 zeros, followed by 100 samples of a CW tone, followed by 1,000 more zeros.
In Linux and OSX, run create_samples.sh. In Windows, run create_samples.bat. This script make take a few moments to complete.
Executing the Example Scripts
Two bladeRF-cli scripts, master.txt and slave.txt, are provided for this example.
The master.txt script configures the "master" device to output its reference clock on the SMB connector (J62), arm a TX "master" trigger, and arm an RX "slave" trigger.
Note that even though both the RX and TX paths are on the same device, one of these must assume the "master" trigger role that will output the trigger signal. Internally, the other path with receive this -- it is very important that both not be configured as "master", as this would cause contention over the trigger signal.
In a multi-device configuration, especially for this master-slave setup, it is recommended to run the bladeRF-cli in a manner that specifies the device to open via serial number.
Run bladeRF-cli -p to see a list of available devices. For example:
$ bladeRF-cli -p

Backend: libusb
Serial: e93f190c76e987cd7f462026f965a1a1
USB Bus: 1
USB Address: 13

Backend: libusb
Serial: b74ed347390d35c29923e80f64c9d904
USB Bus: 12
USB Address: 8

For this example, the "master" is the device with serial number b57... and the "slave" is the device with serial number e93....
In one terminal, run the master.txt script:
$ bladeRF -d '*:serial=b74' -s master.txt -i
In another terminal, run the slave.txt script:
$ bladeRF -d '*:serial=e93' -s slave.txt
At this point, both devices' sample streams are blocked and awaiting a trigger. In the "master" console, fire the trigger via:
trigger j71-4 tx fire
Wait for the RX and TX operations complete via the commands:
rx wait; tx wait
It will most likely be the case that these operations have finished before you can type these commands. They will return immediately if this is true.
Viewing the Results
The results may be viewed using [Octave] 1 or [MATLAB] 2.
Run one of these programs in this directory and execute the plot_samples function provided in this directory. This script will load and plot samples from the master_tx.csv, master_rx.csv, and slave_rx.csv files located in the current working directory.
Note that in the resulting plot, the first pulse transmitted by the "master" will be red/orange. The signal received by the "master" device is blue. The signal received by the "slave" device is green.
Zoom in to see the first few pulses in detail. The reception of the pulse by the "master" and "slave" devices should be synchronized within +/- 1 samples.
Although the devices' sampling clocks are synchronized, they are not guaranteed to be phase-aligned; the mixers in each device operate using independent PLLs. However, the phase offset between the synchronized devices should remain fixed. This allows for opportunities to determine and compensate for phase offsets.
Lastly, there is a fixed offset between the transmission of the signal by the "master" device, and its reception. This length of this offset is determined by the TX chain in the FPGA and LMS6002D, and should remain a constant value. Thus, one can make a priori assumptions about this value after quantifying it for a particular FPGA version. (Changes to the FPGA code could alter this value.)