SETTING X-Y TABLE ZERO (CUTTER METHOD)

There are several ways to set the X-Y zero on a mill. The use of a “Dial Indicator” or an “Edge Finder” are common methods but using the actual tool is also a common  Machine Shop Practice.

- Measure the diameter of the cutter you are going to use

- After mounting the cutter in the spindle, turn on the spindle and lower the “QUILL” until the cutters side edge can easily touch the side of your work piece.

- Slowly turn the “TABLE CRANK” of the desired axis you wish to set moving the cutter slowly towards the side of your work piece.

- Gently touch the side of your work piece with the spinning cutter so that you only remove a small amount of material (less than .001)

- Turn off the spindle and raise the cutter using “QUILL HANDLE”.

- Loosen the “AXIS DIAL LOCKNUT” and set “AXIS DIAL” to zero.

- You can now adjust for you cut by using the “TABLE CRANK”

NOTE: If you wanted to set the center of your spindle to the EDGE of your part you would simply move the table ½ the diameter of your cutter and re-set the “AXIS DIAL”.