## Slide 1: Chapter 12 Transportation

## Slide 2: Learning Objectives
To provide an overview of transportation infrastructures in several countries
To identify the five modes of transportation and learn about their respective characteristics
To discuss intermodal transportation
To familiarize you with several types of transportation specialists
To learn how different types of regulation impact transportation
To identify the legal classification of transportation carriers

## Slide 3: Transportation: Key Terms
  Accessorial service
  Barge
  Broker
  Common Carrier
  Consignee
  Contract carrier
  Container
  Dept. of Transportation
  Dimensional (dim) weight
  Excess capacity
  Exempt carrier
  Freight forwarder
  Intermodal transportation
  Land bridge services
  Less-than-truckload (LTL)
  Line-haul
  Lock
  Parcel carriers
  Piggyback transportation

## Slide 4: Transportation: Key Terms
  Private carriers
  Rail gauge
  Shippers’ association
  Slurry systems
  Surface Transportation Board
  TEU
  Terminal
  Ton miles
  Transportation
  Truckload (TL)
  Unit load devices (ULD)
  Department of Transportation (DOT)

## Slide 5: Transportation
Transportation is the movement of goods and people between two points.

## Slide 6: Transportation
Transportation influences or is influenced by the following logistics activities:
  Transportation costs are affected by node location
  Inventory requirements are influenced by mode
  Packaging requirements are dictated by mode
  Materials handling equipment and design of the docks are dictated by mode
  Maximum consolidation of loads achieved with order-management technology reduces costs
  Customer service goals influence carrier choice

## Slide 7: Transportation
Five different types or modes of transportation include:
  Air
  Motor carrier (truck)
  Pipeline
  Rail
  Water

## Slide 8: Overview of Transportation Infrastructure
  Wide disparities in the various infrastructures exist between highly populated countries
  Lack of infrastructure makes it difficult to use that mode domestically

## Slide 9: Transportation Infrastructure (2006)
 | Brazil | China | India | UK | US
Air (runway > 10k ft.) | 8 | 54 | 17 | 8 | 191
Highway (paved, km) | 95K | 1448K | 2411K | 388K | 4165K
Pipeline (oil, km) | 5.2K | 14.5K | 5.6K | 6.4K | 244.6K
Broad gauge rail (km) | 4.9K |  | 45.7K | 0.5K | 
Std gauge rail (km) | 0.2K | 71.9K |  | 16.8K | 227.7K
Narrow gauge rail (km) | 23.9K |  | 14.4K |  | 
Water (inland, km) | 50K | 124K | 14.5K | 3.2K | 41K
Area (km2) | 8544K | 9806K | 3167K | 244.8K | 9162K

## Slide 10: Transportation Infrastructure (2010)
 | Brazil | China | India | UK | US
Air (runway > 10k ft.) | 7 | 63 | 21 | 9 | 189
Highway (paved, km) | 96K | 3584K | 3320K | 394K | 4375K
Pipeline (oil, km) | 4.5K | 20.1K | 7.7K | .7K | 244.6K
Broad gauge rail (km) | 5.7K |  | 52.8K | 0.3K | 
Std gauge rail (km) | 0.2K | 77.1K |  | 16.2K | 226.4K
Narrow gauge rail (km) | 22.9K | .8K | 8.5K |  | 
Water (inland, km) | 50K | 110K | 14.5K | 3.2K | 41K
Area (km2) | 8544K | 9806K | 3167K | 244.8K | 9162K
https://www.cia.gov/library/publications/the-world-factbook/rankorder/2053rank.htm

## Slide 11: Selecting Transportation Modes
Attributes
Cost
Speed (transit time from pickup to delivery)
Reliability (consistency of delivery)
Capability (amount of different types of product)
Capacity (volume/weight can be carried at one time)
Flexibility (ability to deliver the product to customer)

## Slide 12: Airfreight
  Airfreight
    Generally the fastest mode
    Expensive
    Accessorial service, if needed, adds cost and time
    Best suited for high-value, lower-volume urgent, perishable or time-specific deliveries
    Dimensional weight used for rates

## Slide 13: Airfreight
Advantages:
Speed (line-haul)
Disadvantages:
Cost
Flexibility (need of accessorial service)
Limited capacity
  Boeing 737: 10 tons; 777: 60 tons, 747: 100 tons
  Airbus A-380: 150 tons
Applicable: high-value, low-volume

## Slide 14: Airfreight
  Examples of products that move by air:
    Auto parts and accessories
    Cut flowers and nursery stock
    Electronic or electrical equipment, i.e. iPods
    Fruits and vegetables
    Machinery and parts
    Metal products
    Photographic equipment, parts, and film
    Printed matter
    Wearing apparel

## Slide 15: Airfreight
  Airfreight reliability is problematic due to delays caused by:
    Weather
    Congestion and resultant delays with air passenger transportation (belly freight)

## Slide 16: Motor Carriers
  Motor Carriers
    Most important business user of the Interstate Highway System
    Primary advantage is flexibility
    Cost is generally lower when compared to airfreight
    LTL vs. TL

## Slide 17: Motor Carriers
Advantages:
Flexibility
Capability
Disadvantages:
Cost (only cheaper than airfreight)
Limited capacity: 40 tons (Interstate Hwy)

## Slide 18: LTL Carriers
Less-than-truckload (LTL)
  150 to 10,000 pounds
  Too big to be handled manually, too small to fill a truck
  LTL trucks carry shipments from many shippers
  Prominent LTL carriers include:
    ABF Freight System
    FedEx Freight
    UPS Freight
    YRC (formerly Yellow Freight and Roadway)

## Slide 19: LTL Carriers
Less-than-truckload (LTL) (continued)
  Process
    Local pick-up
    Origin terminal used to load aboard line haul
    Line haul to terminal near destination
    Destination local delivery on smaller trucks
    Consignee receives

## Slide 20: Pipelines
Pipelines
  Only mode without vehicles
  Most reliable mode
  Tend to be the slowest mode
  Accommodates only liquid, liquefiable or gaseous products
  Capable of transporting large product volumes
  High fixed costs, but relatively low cost per unit due to large product volume

## Slide 21: Pipelines
Advantages:
No need for vehicles and vehicle operators
Reliability
Capacity
Disadvantages:
One-way
Limited capability
High Initial Cost
Flexibility

## Slide 22: Railroads
Railroads
  U.S. dominated by four carriers
    Burlington Northern (BN)
    CSX
    Norfolk Southern (NS)
    Union Pacific
  Domination limits service and pricing options

## Slide 23: Railroads
  Neither “best” or “worst” on any of the six attributes
  Superior to air, motor, and pipeline, but inferior to water when transporting different kinds of products
  Less flexibility, but more when compared to air, water, and pipeline
  Superior to air and motor with regards to volume, but inferior to pipeline and water
  Less expensive than air and motor, but more expensive than pipeline and water
  Faster than pipeline and water, but slower than air and truck
  Applicable: low-value, high-volume

## Slide 24: Water
Water
  Relatively inexpensive
  Focus on lower value bulk commodities handled by mechanical means
  Many different kinds of products can be carried
  Carry greater volumes than rail or truck
  Slow average speeds
  Somewhat unreliable

## Slide 25: Water
Advantages:
Cost
Disadvantages:
Speed (6 mph)
Flexibility
Applicable: low-value bulk commodities

## Slide 26: Transportation Mode Comparison
 | Cost ¢/ton-mile | Transit Time | Reliability | Loss & Damage
Rail | 2.28 | 3 | 4 | 5
Truck | 26.19 | 2 | 3 | 4
Water | 0.74 | 5 | 5 | 2
Pipeline | 1.46 | 4 | 2 | 1
Air | 61.20 | 1 | 1 | 3

## Slide 27: Intermodal Transportation
Intermodal transportation refers to transportation when using a container or other equipment that can be transferred from the vehicle of one mode to the vehicle of another mode without the contents being reloaded or disturbed.
Two or more modes are employed to utilize advantages of each while minimizing their disadvantages
  Piggyback transportation

## Slide 28
Figure 12-2: RoadRailer Trailer

## Slide 29: Intermodal Transportation
Containers
  Large reusable steel boxes used for intermodal shipments
  Source: http//en.wikipedia.org/wiki/Shipping_containers.
  Provide significant reduction in freight handling costs
  Are interchangeable among rail, truck, and water carriers
  Airfreight containers (ULDs) are designed specifically for fuselage
  Are measured by TEU’s
  Allowed for land bridge services

## Slide 30: Intermodal Transportation
Advantages:
Uses 2 or more modes to utilize the advantages of each mode while minimizing the disadvantages
Using container or other equipment (transfer from mode to mode without reloading)

## Slide 31: Transportation Specialists
Freight forwarders
  Buy space at TL (truckload) rate and sell at somewhat less than LTL rate
  Pick-up and deliver; motor carriers or railroads do line-haul

## Slide 32: Transportation Specialists
Air forwarders
  Consolidate shipments
  Tender to airlines in containers ready for loading
  Forwarders provide retailing function
  Airline provides wholesaling function
Shipper’s associations
  Similar to air and freight forwarders but are not-for-profit organizations
  Primarily focused on achieving the lowest rates for members

## Slide 33: Transportation Specialists
Brokers
  A facilitator who brings together a buyer and seller
  May consolidate LTL shipments and then give to truckers, forwarders, or shippers’ associations
3PLs
  Find clients with complimentary needs to maximize equipment utilization

## Slide 34: Transportation Specialists
Parcel carriers
  Parcels are packages weighing up to 150 pounds
  Parcel carriers are companies that specialize in transporting parcels
  Parcel carriers include:
    USPS
    UPS
    FedEx
    Greyhound Package Express

## Slide 35: Transportation Regulation
Five modes are influenced by federal, state and local government regulations
  Examples:
    Mandatory retirement age for pilots in U.S.
    Placement of lighting on truck trailers
Regulation
  Costs money
  Needs to be codified
  Is enforced by government agencies

## Slide 36: Transportation Regulation
Level and degree of regulation varies from country to country
  i.e. industrialized countries tend to have more stringent transportation equipment emissions regulations when compared to those of less industrialized countries
Logisticians must understand
  Relevant transportation regulations
  Cost and service implications of regulations

## Slide 37: Federal Regulation of Transportation in U.S.
Environmental
  Environment Protection Agency (EPA) is the federal regulatory agency established to protect human health and the environment
  Current concerns include:
    Noise and air pollution
    Resource conservation

## Slide 38: Federal Regulation of Transportation in U.S.
Safety
  Department of Transportation (DOT) is the federal agency responsible for transportation safety regulations for all five modes
  Federal Aviation Administration (FAA) has primary responsibility for air transportation safety
  Federal Motor Carrier Safety Administration (FMCSA) is focused on reducing crashes, injuries, and fatalities involving large trucks and buses.

## Slide 39: Federal Regulation of Transportation in U.S.
Safety (continued)
  Office of Pipeline Safety (OPS) is responsible for safety considerations for natural gas and liquid pipelines
  Federal Railroad Administration (FRA) has primary responsibility for safety in the U.S. railroad industry
  U.S. Coast Guard (USCG) has safety regulation responsibilities for marine safety considerations

## Slide 40: Federal Regulation of Transportation in U.S.
Economic
  Refers to control over business practices and activities such as entry and exit, pricing, service, accounting, and financial issues, and mergers and acquisitions
  Regulation began in the 1870’s due to a belief that transportation companies would not act in the public’s best interest without government regulation

## Slide 41: Federal Regulation of Transportation in U.S.
Economic (continued)
  Interstate Commerce Commission (ICC) has authority over rail, motor, inland water, and oil pipelines
  Civil Aeronautics Board (CAB) has authority over air transportation

## Slide 42: Federal Regulation of Transportation in U.S.
Economic (continued)
  Due to deregulation
    Civil Aeronautics Board (CAB) was eliminated
    Interstate Commerce Commission (ICC) was eliminated with functions transferred to a new agency, the Surface Transportation Board (STB)
  Economic deregulation has allowed greater freedom with respect to pricing and service options

## Slide 43: Legal Classification of Carriers
Transportation carriers are classified as either
  For-hire
    Common
    Contract
    Exempt
  Private
Classification is important because different levels of economic regulation are applicable to different carriers

## Slide 44: Legal Classification of Carriers
Common carriers serve the general public
Contract carriers offer specialized service to customers on a contractual basis
  No obligation to serve the general public or to treat customers on an equal basis
Exempt carriers are exempted from economic regulation due to legislation
Private carriers are companies whose primary business is other than transportation and provide their own transportation service
  Also exempt from economic regulation

## Slide 45: Private Transportation
Private transportation is used when firms own and operate their own trucks, railcars, barges, ships, and/or airplanes
  Wal-Mart has largest private truck fleet in U.S.
    7,767 tractors and 26,117 trailers
Private trucking provides
  Improved level of customer service
  Advertising on the trucks
  May be less expensive

## Slide 46
Located in Crown Point, Indiana (1910)
Company Facts:
Products:
Large off-road vehicles (airport snowplows, airport crash trucks, oil-field drilling equipment, etc.)
Case 12-1 HDT Truck Company
Plant Capacity:
2 trucks assembled / day (single shift)
Max. 3 for large order of identical trucks
At least 4-mo backlog

## Slide 47
Received an order of 50 heavy trucks from Saudi Arabia
Deliver on or before July 1, 2003
Priced at $172,000/truck FAS at Doha
Production is scheduled from April 2 ~ April 29 (2.5/day)
Current Issues:
Case 12-1 HDT Truck Company
People Involved:
Norman Pon (Treasurer)
Chris Reynolds (Production)
Vic Guillou (Sales)
Gordon Robertson (President)
Bob Vanderpool (Traffic)
Bob Guider (Int’l Freight Forwarded, Chicago)
Eddie Quan (Ship Broker, NY)

## Slide 48
Case 12-1 HDT Truck Company

## Slide 49
Components will arrive from April 1 to April 10
Term for payment: 1/10 (1% discount if paid in 10 days)
Line of credits: 8%
Account Payables:
Case 12-1 HDT Truck Company

## Slide 50
Case 12-1 HDT Truck Company
Alternatives for Shipping:
Charter from Chicago:
  Nola Pino, Ready on May 1, $2,400/day for 30 days
  Loading & Unloading: $40/truck
  To Chicago (Railroad Flatcar): $180/truck
  Travel Time: 1 day + 1 day waiting (L)
  Wharfage Charge: $2/ft x 535 ft x 1 day
  Loading & Stowing: $4,000 for 50 trucks
  Seaway Tolls: $54/truck
  Unloading (at Doha): $4,200 for 50 trucks
  Marine insurance: $210 / truck
Ship from Baltimore:
  To Baltimore (Railroad Flatcar): 2 trucks/flatcar, $1,792/flatcar
  Loading & Unloading: $120/flatcar
  Travel Time: 4 days + 3 days waiting (L&UL)
  Handling at Baltimore: $200/truck
  Ocean freight: $1,440/truck + $150/truck for insurance

## Slide 51
Case 12-1 HDT Truck Company
Questions:
Assume you are Vanderpool. Draft the comparison Pon just requested.
Which of the two routing alternatives would you recommend? Why?
Assume that the buyer in Saudi Arabia has made other large purchases in the United States and is considering consolidating all of its purchases and loading them onto one large ship, which the buyer will charter. The buyer contacts HDT and, although acknowledging its commitment to buy FAS Doha, asks how much HDT would subtract from the $172,000 per truck price if the selling terms were changed to FOB HDT’s Crown Point plant. How much of a cost reduction do you think HDT should offer the buyer? Under what terms and conditions?

## Slide 52
Case 12-1 HDT Truck Company
Questions:
Answer question 3 with regard to changing the terms of sale to delivery at port in Baltimore. The buyer would unload the trucks from the railcars.
Is there an interest rate that would make HDT change from one routing to another? If so, what is it?
Assume that it is the year 2005 and the cost to HDT of borrowing money is 12% per year. Because the buyer will pay for trucks as they are delivered, would it be advantageous for HDT to pay overtime to speed up production, ship the trucks as they were finished via the Port of Baltimore, and collect their payment earlier? Why or why not?